## Slide 1: Runtime Monitoring for Safety-Critical Embedded Systems
Ph.D. Defense
Aaron Kane
1/20/15
Prof. Philip Koopman (Advisor)
Prof. Anupam Datta
Prof. Andre Platzer
Dr. Chuck Weinstock

## Slide 2: Outline
Intro
Problem
Scope
Contributions
Intro
Architecture
Formalisms
Monitor Implementation
Monitor Evaluation
Conclusion

## Slide 3: Introduction
Building complex embedded systems is difficult
Notes: !!!!!! We are going to focus on ground vehicles, but other types of systems are similar…

## Slide 4: Introduction
Building complex embedded systems is difficult
Complexity limits traditional verification techniques
  Costs, state space explosion, etc.
Runtime verification (RV) is a lightweight technique to provide checking of system at runtime
  Handles scaling complexity/abstraction in a nice way
  Complementary to other verification techniques!
Notes: RV also lets us look at different system levels

## Slide 5: Runtime Verification (RV)
Runtime verification is the general method of taking an execution trace and a formal policy and deciding if the trace satisfies the policy
Runtime verification generally performed by monitors
  Different methods: timed automata, logic-based, petri nets
φ
System
Trace
Specification
Monitor
Satisfy/Violate
Verdict
Notes: Offline or Online
Can run offline (log checking) or online (runtime)
  Many different names, all similar idea

## Slide 6: Problem
Existing RV techniques are generally not aimed at safety-critical systems
  And especially real-time, distributed, multi-vendor, commercial-off-the-shelf, black-box components
Code instrumentation is common
  Safety-critical monitoring constraints (from Pike et. al.)
    Functionality
    Certifiability
    Timing
    Size, Weight, and Power (SWaP)
Notes: The problem is that existing rv techniques are not generally aimed at real-time safety critical systems.
Many of these methods aren’t built to handle real-time, distributed systems.
Many modern complex systems such as cars are built as distributed systems made up of COTS or multi-vendor components that may be black box.
A primary issue is code instrumentation…
They actually change the target system’s code to either add an inline monitor or to expose necessary state. This has two problems. 1) you can’t do code instrumentation on black box systems, and 2) it can affect the system in a bad way.
We’ll focus on goodloe&pike’s FaCTS constraints. Functionality and timing…
----- Meeting Notes (1/14/15 14:09) -----
citation for FaCTS
emphasize SWaP

## Slide 7: Thesis Scope
Primary research questions:
  How do the constraints of safety-critical embedded systems affect runtime monitoring?
  What monitor architectures fit these constraints?
  Can we build monitor which fits constraints and can detect useful violations?
Focused on testing
Need good requirements!
Getting them is out of scope
Assuming correct monitor implementation, trusted input
Notes: These problems bring us to these primary research questions…
----- Meeting Notes (1/14/15 14:09) -----
safety critical embedded constraints

## Slide 8: Contributions
Identified suitable RV architecture for safety-critical embedded systems
Provide monitoring framework with formal algorithm and semi-formal system mapping
Demonstrate the feasibility and show performance characteristics of this monitoring framework
Notes:   Passive external broadcast bus monitor
  Semi-formal mapping, specification language, algorithms, specification and safety-case patterns
  Detect specification violations on logs of real systems under test

## Slide 9: Contributions
Identified suitable RV architecture for safety-critical embedded systems
Provide monitoring framework with formal algorithm and semi-formal system mapping
Demonstrate the feasibility and show performance characteristics of this monitoring framework
Passive External Bus Monitor
No Instrumentation
Potentially Bolt-on
Notes: ----- Meeting Notes (1/14/15 14:09) -----
Mention this more!!!

## Slide 10: Contributions
Identified suitable RV architecture for safety-critical embedded systems
Provide monitoring framework with formal algorithm and semi-formal system mapping
Demonstrate the feasibility and show performance characteristics of this monitoring framework
Semi-Formal Mapping
Specification Logic
Monitoring Algorithm
Specification Patterns
Safety Case Patterns
Notes:   I provide an end-to-end semi-formal monitoring framework…

## Slide 11: Contributions
Identified suitable RV architecture for safety-critical embedded systems
Provide monitoring framework with formal algorithm and semi-formal system mapping
Demonstrate the feasibility and show performance characteristics of this monitoring framework
PC-based Offline Log Monitor
ARM-based real-time CAN Monitor
Checked logs from real systems under test
Autonomous vehicle logs
Potential safety violations detected
Real-time CAN log replay
Specification violations detected

## Slide 12: Outline
Motivation
Use Cases
Architecture
Usability Patterns
Intro
Architecture
Formalisms
Monitor Implementation
Monitor Evaluation
Conclusion

## Slide 13: Motivation
Emphasized the following constraints
  Potentially black-box components
    No program instrumentation
    Limited observability
  Bolt-on monitoring preferred
    Connect to unprepared systems
    Promotes isolation
  Using monitor should not require specialists
    Not enough specialists, won’t get used
  Minimize overall costs
    Additional SWaP, integration, etc.
Leads to external bus monitor
X0
Xn
Data Bus Interconnect
Monitor
System Under Observation
Monitoring Architecture
External Bus Monitor
(Adapted from [1])
Notes: Gotta go fast
Careful describing formal methods uptake **reluctant**
Why lead to external bus monitor:
other architectures require more instrumentation/alteration
distributed bus mon
extra monitoring bus
----- Meeting Notes (1/14/15 14:09) -----
Careful with formal methods
**Industry reluctant to use formal methods
Why does this imply external bus monitor
as opposed to inline/attached
what other sols were rejected

## Slide 14: Use Cases
Test Oracle
  Mechanism to determine whether a test passed or failed
  Automated oracles support automated testing
  Check observable properties, not internal behavior
Runtime Fault Detector
  May be able to rely on monitor/recovery for safety, reducing criticality of the rest of the system
  Choosing a valid recovery action is difficult
Test Harness
System
Test
Oracle
Pass/Fail
Test Results/Logs
Test Control
Notes:     Can target different abstraction levels or development points

## Slide 15: Prototype Test Oracle Example
Used a prototype monitor as test oracle for hardware-in-the-loop vehicle simulator
  Tested full-speed range adaptive cruise control feature
    Simple rules (e.g., don’t accelerate if too close to target)
Performed black-box robustness testing
  Mostly to exercise system
Found violations of the checked rules
  Features not designed to be robust
  Some caused by inaccurate specification (false positives)
Notes: An early step was to try out using a monitor as a test oracle.
Early on we used a prototype monitor as a test oracle to perform offline monitoring of a HIL simulator at a commercial research lab.
Overly strict – jitter, sampling issues, etc
----- Meeting Notes (1/14/15 14:09) -----
"Prototype" monitor
Some of them were false positives -- nice
Move infront of explanation stuff

## Slide 16: Lessons Learned
External observability is workable
  Does limit monitoring
Need flexible mapping control
  Message period issues
  Discrete value jumps (mode switch/startup)
False positives likely with common specifications
  Need very precise specification to avoid this
  Can use monitor to explore and refine specification
Notes:   Intent estimation can be difficult…

## Slide 17: Architecture Overview
Trace
Spec
SF
Map
Monitor
Algorithm
Action
Controller
Formal
Side
Informal
Side
Monitor
σi
φ
Target System
System Bus
Warning/Log/Steering
Satisfy/Violate
Notes: Emphasize!!! External; Semi-Formal

## Slide 18: External Monitoring
External monitors have strong isolation
  Preserve system functionality/timing
  Potential for modular certification
Pay some SWaP costs for isolation
  Necessary for strong isolation
  Weaker isolation (e.g., independent core) may be ok
Observability issues
  Can only monitor values visible on bus
  Very system dependent
Notes: This is an external monitoring architecture…
Sampling-based monitoring
  Less intrusive, predictable overhead (avoid event bursts)

## Slide 19: Semi-Formal Monitoring
Interface has two purposes
  Convert system state into propositional execution trace
  Provide additional semantic power beyond logic
Split specification into two parts
  Formal system specification in logic
  Semi-formal configuration defines available propositions
Notes: This architecture is also a semi-formal monitoring architecture…
Need to map system to monitor’s model
  Existing monitors use similar interfaces (e.g., MaC filters)
Specification must be able to express desired system properties
  Or monitor won’t get used

## Slide 20: Semi-Formal Monitoring
Provides flexibility
and power
Notes: What this does it provide the necessary flexibility and power to monitor a diverse set of systems

## Slide 21: Semi-Formal Monitoring
Correctness guarantees
Easier traceability
Harder to verify
Provides flexibility
and power

## Slide 22: Semi-Formal Monitoring
Want to specify as much as possible in formal specification
  But, better to use some semi-formal aspects than not monitor at all
Correctness guarantees
Easier traceability
Harder to verify
Provides flexibility
and power
Notes: Verifiable. Unambiguous.
Need to map system to monitor’s model
  Existing monitors use similar interfaces (e.g., MaC filters)
Specification must be able to express desired system properties
  Or monitor won’t get used
----- Meeting Notes (1/14/15 14:09) -----
There's always stuff you can't put in.

## Slide 23: Usability Patterns
Specification patterns help create formal specifications
Safety case pattern provides example of safety case for external monitor integration
Notes: One of our motivating constraints was to make monitoring easier for non-specialists. So

## Slide 24: Specification Pattern

## Slide 25
G1
External monitor does not introduce additional hazards to target system
G2
Monitor does not affect system behavior
G3
Monitor actions do not introduce additional hazards
C1
System Description
System Interface description
C2
S1
Argument by limits of network interface
Safety Case
Pattern
Notes: We also have a safety case pattern. This is an outline of the argument used to show that incorporating an external monitor into a system is safe. It is written in the widely used goal structured notation. The “G” boxes are goals, the rounded “C” boxes are contexts which provide extra information, and the “S” rhombus is a strategy.
This pattern argues that adding an external monitor doesn’t add additional hazards.
----- Meeting Notes (1/14/15 14:09) -----
*general* pattern for external monitors
describe GSN

## Slide 26: Safety Case Pattern
No additional hazards
Integration hazards addressed
Monitor actions hazards addressed
No actions which can cause hazards
CAN configured in silent mode, checked by code review

## Slide 27: Outline
Practical Issues
Algorithm
Intro
Architecture
Formalisms
Monitor Implementation
Monitor Evaluation
Conclusion
Notes: Now we have this architecture and semi-formal front-end, so let’s look at the actual specification and checking algorithm

## Slide 28: Practical Issues
Time-triggered, sampling based monitoring
  Predictable overhead, no execution bursts
  Event triggered networks can be sampled
Use two-valued logic in a three-valued way
  Algorithm delays answering inconclusive questions
    Distinguishes good/bad vs inconclusive trace prefixes
Notes:   Time triggered: Need to match this to trace semantics
  Sample fast enough to see desired properties
Iterative, formula-rewriting based algorithm
  Only need relevant history and current state

## Slide 29: Bounded Logic

## Slide 30: Algorithm Basics
Algorithm is built on residues and history structures
Primary work is done by the reduce() function
  Rewrites residue formula based on history and state
  Used recursively over subformula to build up state history
Notes: Reduce evaluates formulas
----- Meeting Notes (1/14/15 14:24) -----
residue def should be j
i is current timestep, j is step of evaluating residue
Explain reduce in “normal” way – fills in propositions and does syntactic reduction

## Slide 31: Aggressive Algorithm
Notes: Mention what aggressive is.

## Slide 32: Algorithm Walkthrough

## Slide 33: Algorithm Walkthrough

## Slide 34: Algorithm Walkthrough

## Slide 35: Algorithm Walkthrough

## Slide 36: Algorithm Walkthrough
Notes: \begin{align*}
%\varphi &= a \rightarrow \underbrace{\lozenge_{[1,1]} (\xoverbrace{\lozenge_{[0,1]} b}^{\phi})}_{\psi} \\ \\
\varphi &= a \rightarrow \xoverbrace{\lozenge_{[1,1]} (\xunderbrace{\lozenge_{[0,1]}\, b}_{\phi})}^{\psi} \\
%\varphi &= a \rightarrow \lozenge_{[1,1]} (\overbrace{\vphantom{\frac{1}{1}} \lozenge_{[0,1]} b}^{\phi}) \\
S^i_{b} &= \rp{0}{\bot}, \rp{1}{\bot}, \rp{2}{\bot}. \rp{3}{\bot} \\%,\rp{4}{\top} \\
S^i_{\lozenge_{[0,1]} b} &= \rp{0}{\bot}, \rp{1}{\bot}, \rp{2}{\bot}, \rp{3}{\phi}\\%, \rp{4}{\top} \\
S^i_{\varphi} &= \rp{0}{\top} , \rp{1}{\bot}, \rp{2}{\psi}, \rp{3}{\psi}\\%, \rp{4}{\top} \\
\end{align*}

## Slide 37: Algorithm Walkthrough
Notes: ----- Meeting Notes (1/14/15 14:24) -----
mention 3/4 get solved aggressively
Fix period in figure
\begin{align*}
%\varphi &= a \rightarrow \underbrace{\lozenge_{[1,1]} (\xoverbrace{\lozenge_{[0,1]} b}^{\phi})}_{\psi} \\ \\
\varphi &= a \rightarrow \xoverbrace{\lozenge_{[1,1]} (\xunderbrace{\lozenge_{[0,1]}\, b}_{\phi})}^{\psi} \\
%\varphi &= a \rightarrow \lozenge_{[1,1]} (\overbrace{\vphantom{\frac{1}{1}} \lozenge_{[0,1]} b}^{\phi}) \\
S^i_{b} &= \rp{0}{\bot}, \rp{1}{\bot}, \rp{2}{\bot}. \rp{3}{\bot}, \rp{4}{\top} \\
S^i_{\lozenge_{[0,1]} b} &= \rp{0}{\bot}, \rp{1}{\bot}, \rp{2}{\bot}, \rp{3}{\top}, \rp{4}{\top} \\
S^i_{\varphi} &= \rp{0}{\top} , \rp{1}{\bot}, \rp{2}{\top}, \rp{3}{\top}, \rp{4}{\top} \\
\end{align*}

## Slide 38: Formal Monitoring
We have proofs of correctness for this algorithm
  Correctness:
    If a violation is reported then the trace did violate the specification at that step
  Promptness
    If a violation exists at least Δ(φ) time ago, then the violation is reported
Guaranteed prompt and correct answer to the question:
Does the execution trace satisfy the given specification?
Still need to build an accurate trace
Still need a good specification

## Slide 39: Outline
Design Constraints
Hybrid Scheme
Intro
Architecture
Formalisms
Monitor Implementation
Monitor Evaluation
Conclusion

## Slide 40: Implementation Overview
Two implementations based on same codebase
  PC-based offline CSV log monitor
  ARM-based real-time CAN bus monitor
Targeted for real-time embedded:
  No dynamic memory allocation
  No recursion
  Extra optimizations
    Interval based history structures
    Extended Logic
  Hybrid Aggressive/Conservative checking
Notes: Static memory – avoid memory leaks
No recursion – guaranteed stack depth

## Slide 41: Static Memory
Statically allocate data structures
  Bounded logic  known max sizes
Residue formula can be large
  History structures can require a lot of storage
  Use one global formula instead
Notes: We don’t want dynamic memory, but the algorithm uses many lists of things

## Slide 42: No Recursion
Iterative DFS style reduce()
Use traversal stacks since we cannot mark the global tree

## Slide 43: Algorithm Optimizations
Implemented two high-value optimizations
  Interval history structures
    Decrease worst-case runtimes
  Extra logic operators
    Save formula storage space
    Save some execution time
Interval
Lists
Residue
List
Notes:     Intervals decrease average storage space
    doesn’t help with static allocation

## Slide 44: Hybrid Scheme
Aggressive checking can provide early detection of temporal rules
But, it’s much more computationally expensive
  May not always be able to keep up with real-time
  Can be very bursty – depends on trace
Conservative checking has slower response time but relatively constant and shorter execution time
  Only check residues older than delay, guaranteed evaluation
Idea: Combine the approaches
  Obtain worst-case guarantees from conservative
  Use extra time to do as much aggressive checking as possible

## Slide 45: A little scheduling
Essentially a multi-tasking system with 4 tasks:
Some blocking to share structures, all straightforward
Task | Priority | Location
Trace Update | Highest | CAN receive ISR
Structure Update | High | Timer 2 ISR
Conservative Check | High | Timer 2 ISR
Aggressive Check | Low | Main loop
Notes: ----- Meeting Notes (1/14/15 14:24) -----
Structure Update

## Slide 46: Hybrid in action
Simple lab bench setup with instrumentation
  One 100ms CAN message (would see more data in a real system)
  Checking 200 residues (<0,200> val) on top of heartbeat rules
  ~23ms idle with 25ms loop
Trace Update
Conservative Check
Aggressive Check
Idle
Notes: ----- Meeting Notes (1/14/15 14:24) -----
grid lines

## Slide 47: Outline
Offline Vehicle Logs
Replayed CAN Logs
Intro
Architecture
Formalisms
Monitor Implementation
Monitor Evaluation
Conclusion
Notes: SHOULD BE AROUND 48 minutes!
~11 minutes from here to end

## Slide 48: Offline Vehicle Log Checking
Logs from test drive of autonomous research vehicle
  Approximately 16 hour drive
  Primarily looking at lane centering feature
Ad-hoc rule elicitation
  Not much info available

## Slide 49: Monitored Rules
No violations of Rule #0
Violations of Rules #1/2
  Didn’t always match – sensor accuracy is important
  Need more info to know if these are real problems
Notes: ----- Meeting Notes (1/14/15 14:24) -----
disengaged -- debouncing

## Slide 50: Embedded Replay
Real-time replay of CAN logs from system robustness testing
<0.01% average message timing error
  Sub-ms absolute error (fast enough for 25ms monitoring)
Had some system documentation
  Real derived rules!

## Slide 51: Monitor Specification

## Slide 52: Monitoring Results
Detected Heartbeat and transition violations
  Three heartbeat violation types detected
    Late/missing heartbeat
      Real violation
    On-time heartbeat with heartbeat status set to 0
      May be a problem
    Bad heartbeat counter value
      False positive caused by test controlled messages
  Transition violations were also test-induced FP
Notes: ----- Meeting Notes (1/14/15 14:24) -----
Test-rig caused false positive -- induced by design
not monitor caused

## Slide 53: Late Heartbeat
Unclassified: Distribution A: Approved for Public Release. OPSEC review #26162

## Slide 54: Bad Counter
Invalid Counter
Unclassified: Distribution A: Approved for Public Release. OPSEC review #26162
Notes: ----- Meeting Notes (1/13/15 22:54) -----
put invariant on slide?

## Slide 55: Outline
Future Work
Conclusion
Intro
Architecture
Formalisms
Monitor Implementation
Monitor Evaluation
Conclusion
Notes: Detected violations of realistic properties on real system logs
FEASIBLE!
Specification quality is very important

## Slide 56: Future Work
Recovery
  Hard to do safely
  Emergency stop not always best choice
    Prefer to controlled stop if possible
  Need to diagnose faults to choose viable recovery
Semi-formal Specification Language
  More formal definition of interface between system and monitor
  Domain Specific Language can be designed to help verification of interface

## Slide 57: Conclusions
Identified suitable RV architecture
Provided an end-to-end monitoring framework for safety-critical embedded
Real-time monitoring of CAN networks is feasible
Passive External Bus Monitor
Handles Black-box components
No Instrumentation
Potentially Bolt-on

## Slide 58: Conclusions
Identified suitable RV architecture
Provided an end-to-end monitoring framework for safety-critical embedded
Real-time monitoring of CAN networks is feasible
Semi-formal mapping
Specification Logic
Algorithms
Correctness Proofs
Specification Patterns
Safety Case Patterns

## Slide 59: Conclusions
Identified suitable RV architecture
Provided an end-to-end monitoring framework for safety-critical embedded
Real-time monitoring of CAN networks is feasible
Checked logs from real systems under test
Found potential violations in offline logs from autonomous research vehicle
Detected violations on CAN bus

## Slide 60: Questions?
Thank you
[1] Goodloe, A. & Pike, L. Monitoring distributed real-time systems: a survey and future directions NASA Langley Research Center, 2010

## Slide 61: Extras

## Slide 62: Info Extras
Keeping these for now, just because

## Slide 63: Evaluation Overview
Detected violations of realistic properties on real system logs
  Both offline logs and live CAN
  This type of monitoring is feasible
Specification quality is very important
  “Accuracy” affects false positive rate
  Take initialization into account

## Slide 64: Optimization/Scalability Check
Using PC-based implementation
Artificial logs (all false/true, alternating, etc)
See how optimizations and algorithm works

## Slide 72: Practical Issues
Time-triggered, sampling based monitoring
  Predictable overhead, no execution bursts
  Event triggered networks can be sampled
Iterative, formula-rewriting based algorithm
  Only need relevant history and current state
Use two-valued logic in a three-valued way
  Algorithm delays answering inconclusive questions
    Distinguishes good/bad vs inconclusive trace prefixes
0
1
2
3
4
5
F
F
T
T
F
F
X:
Notes:   Time triggered: Need to match this to trace semantics
  Sample fast enough to see desired properties
  Bounded logic and “real” time – trace will progress
----- Meeting Notes (1/14/15 14:09) -----
add bullet -- sample into event triggered
better discussion of prefixes -- how does two-valued logic work
Need example of two-valued logic in three-valued way
“it will rain today or tomorrow” Yes/No

## Slide 73: PROOF STUFF

## Slide 74: Wait Delay

## Slide 75: Storage Delay

## Slide 76: Residue Properties

## Slide 78: Algorithm
Notes: \begin{algorithmic}[1]
%\STATE Recognize formulas for which we build structures
\STATE For all recognized formulas $\psi \in \mathbf{tempSub}(\varphi)$: $S^{-1}_{\psi} \leftarrow \emptyset$
\STATE $S^{-1}_\varphi \leftarrow \emptyset$
\STATE $i \leftarrow 0$
\LOOP
\STATE Obtain $(\sigma_i,\tau_i$ from trace
\STATE Extend $\tau$ with next timestamp $\tau_i$
%\STATE Obtain $(\sigma_i,\tau_i)$ from trace
\FOR{every $\psi \in \mathbf{tempSub}(\varphi)$ in increasing size}
\STATE $S^i_{\psi} \leftarrow \mathbf{incrS(} S^{i-1}_{\psi}, \mathbb{S}^i_{\psi}, \sigma_i, \tau, i)$
\ENDFOR
\STATE $S^i_{\varphi} \leftarrow \mathbf{incrS(} S^{i-1}_{\varphi}, \mathbb{S}^i_{\varphi}, \sigma_i, \tau, i)$
\FOR{all $\rp{j}{\bot} \in S^i_{\varphi}$}
\STATE \texttt{Report violation on $\sigma$ at position $j$}
\ENDFOR
\STATE $i \leftarrow i + 1$
\ENDLOOP
\end{algorithmic}

## Slide 79: Reduce
Notes: \begin{align*}
\mathbf{reduce}(\sigma_i,\tau, i,\mathbb{S}^i_{\top},\rp{j}{\top}) &= \rp{j}{\top} \\
\mathbf{reduce}(\sigma_i,\tau, i,\mathbb{S}^i_{\bot},\rp{j}{\bot}) &= \rp{j}{\bot} \\
\mathbf{reduce}(\sigma_i,\tau, i,\mathbb{S}^i_{p},\rp{j}{p}) &= \rp{j}{\sigma_i(p)} \\
\end{align*}
\begin{align*}
\mathbf{reduce}(\sigma_i,\tau, i,\mathbb{S}^i_{\neg \psi},\rp{j}{\neg \psi}) = \left\{
\begin{aligned}
\text{Let } &\psi' \leftarrow \mathbf{reduce}(\sigma_i, \tau, i, \mathbb{S}^i_{\psi}, \rp{j}{\psi}) \\
&\psi'' \leftarrow \mathbf{simplify}(\neg \psi') \\
&\textbf{return } \rp{j}{\psi''} \\
\end{aligned} \right. \\
\end{align*}
\begin{align*}
\mathbf{reduce}(\sigma_i,\tau, i,\mathbb{S}^i_{\alpha \vee \beta},\rp{j}{\alpha \vee \beta}) = \left\{
\begin{aligned}
\text{Let } &\alpha' \leftarrow \mathbf{reduce}(\sigma_i, \tau, i, \mathbb{S}^i_{\alpha}, \rp{j}{\alpha}) \\
&\beta' \leftarrow \mathbf{reduce}(\sigma_i, \tau, i, \mathbb{S}^i_{\beta}, \rp{j}{\beta}) \\
&\phi' \leftarrow \mathbf{simplify}(\alpha' \vee \beta') \\
&\textbf{return } \rp{j}{\phi'} \\
\end{aligned} \right. \\
\end{align*}

## Slide 80: Reduce (until)
Notes: %%% TAU UNTIL
\begin{align*}
\mathbf{reduce}(\sigma_i,\tau, i,\mathbb{S}^i_{\alpha\, \mathcal{U}_{[l,h]}\, \beta} ,\rp{j}{\alpha\, \mathcal{U}_{[l,h]}\, \beta}) = \left\{
\begin{aligned}
&\text{let } a_a \leftarrow min(\{k | \tau_j \leq \tau_k \leq \tau_j+h \wedge \rp{k}{\bot} \in S^i_\alpha \},i) \\
% a_u
& a_u \leftarrow min({k| \tau_j \leq \tau_k \leq \tau_j+h \wedge \rp{k}{\alpha'} \in S^i_\alpha \wedge \alpha' \not\equiv \top},i) \\
% b_a
& b_a \leftarrow min(\{k | \tau_j+l \leq \tau_k \leq \tau_j+h \wedge \rp{k}{\beta'} \in S^i_\beta \wedge \beta' \neq \bot\}) \\
% b_t
&b_t \leftarrow min(\{k | \tau_j+l \leq \tau_k \leq \tau_j+h \wedge \rp{k}{\top} \in S^i_{\beta} \}) \\
% b_n
&b_n \leftarrow \top \text{ if } (\tau_i - \tau_j \geq \Delta^w(\psi)) \\ & \quad \quad \quad \quad \quad \wedge \forall k.(\tau_j+l \leq \tau_k \leq \tau_j+h). \rp{k}{\bot} \in S^i_{\beta} \\
&\text{if } b_t \neq \emptyset \wedge a_u \geq b_t \\
& \quad\mathbf{return} \rp{j}{\top} \\
&\text{else if } (b_a \neq \emptyset \wedge a_a < b_a) \text{ or } b_n = \top\\ & \quad\mathbf{return} \rp{j}{\bot} \\
&\text{else} \\
& \quad\mathbf{return} \rp{j}{\alpha\, \mathcal{U}_{[l,h]}\, \beta}
\end{aligned} \right. \\
\end{align*}

## Slide 81: Reduce (since)
Notes: %%% TAU SINCE
\begin{align*}
\mathbf{reduce}(\sigma_i,\tau, i,\mathbb{S}^i_{\alpha\, \mathcal{S}_{[l,h]}\, \beta} ,\rp{j}{\alpha\, \mathcal{S}_{[l,h]}\, \beta}) = \left\{
\begin{aligned}
&\text{let } a_a \leftarrow max(\{k | \tau_j-h \leq \tau_k \leq \tau_j \wedge \rp{k}{\bot} \in S^i_\alpha \},i) \\
% a_u
& a_s \leftarrow max({k| \tau_j-h \leq \tau_k \leq \tau_j \wedge \rp{k}{\alpha'} \in S^i_\alpha \wedge \alpha' \not\equiv \top},i) \\
% b_a
& b_a \leftarrow max(\{k | \tau_j-h \leq \tau_k \leq \tau_j-l \wedge \rp{k}{\beta'} \in S^i_\beta \wedge \beta' \neq \bot\}) \\
% b_t
&b_t \leftarrow max(\{k | \tau_j-h \leq \tau_k \leq \tau_j-l \wedge \rp{k}{\top} \in S^i_{\beta} \}) \\
% b_n
&b_n \leftarrow \top \text{ if } (\tau_i - \tau_j \geq \Delta^w(\psi)) \\ & \quad \quad \quad \quad \quad \wedge
\forall k.(\tau_j-h \leq \tau_k \leq \tau_j-l). \rp{k}{\bot} \in S^i_{\beta} \\
%%
&\text{if } b_t \neq \emptyset \wedge a_s \leq b_t \\
& \quad\mathbf{return} \rp{j}{\top} \\
&\text{else if } (b_a \neq \emptyset \wedge a_a > b_a) \text{ or } b_n = \top\\ & \quad\mathbf{return} \rp{j}{\bot} \\
&\text{else} \\
& \quad\mathbf{return} \rp{j}{\alpha\, \mathcal{S}_{[l,h]}\, \beta}
\end{aligned} \right. \\
\end{align*}

## Slide 82: IncrS is correct
Notes: \begin{align*}
\mathbf{incrS}(S^{i-1}_\psi, \mathbb{S}^i_{\psi}, \sigma_i, \tau, i) = %\left\lbrace
%\begin{aligned}
\left(\bigcup\limits_{r \in S^{i-1}_{\psi}} \mathbf{reduce}(\sigma_i, \tau, \mathbb{S}^i_{\psi}, r)\right) \cup \mathbf{reduce}(\sigma_i, \tau, \mathbb{S}^i_{\psi}, \rp{i}{\psi})
%\end{aligned} \right.
\end{align*}
For all states traces $\sigma$, timestamp series $\tau$, timesteps $i$, formulas $\psi$, correct, prompt, and reducible structures $S^{i-1}_{\psi}$, and correct and prompt $\mathbb{S}^i_{\psi}$
if $S^i_{\psi} \leftarrow \mathbf{incrS(}(S^{i-1}_{\psi},\mathbb{S}^i_{\psi}, \sigma_i, \tau_i, i)$ then $S^i_{\psi}$ is correct, prompt, and reducable.
\textit{Proof}. Follows from $\mathbf{reduce}(\ldots)$ preserving correctness/promptness/reducability. \\
%
Since $S^{i-1}_\psi$ is correct/prompt/reducable, it has a residue entry for all $k \in [0,i-1]$ which are all c/r/p. $\mathbf{incrS}(\ldots)$ adds the residue for $i$, so $S^i_\psi$ has all the necessary residues. All the residues from $S^{i-1}$ are c/r/p because $\mathbf{reduce}(\ldots)$ preserves c/r/p. The new reduced residue $\rp{i}{\psi}$ is also c/r/p from the correctness of $\mathbf{reduce}(\ldots)$: $\mathbb{S}^i_\psi$ is correct and prompt, and $i=j$.

## Slide 83: Reduce is correct
Notes: For all timesteps $i,j$ where $j\leq i$, formulas $\phi,\psi$, traces $\sigma$, timestamp series $\tau$, and history structures $\mathbb{S}^i_{\psi}$ such that $\mathbb{S}^i_{\psi}$ is correct/prompt/reducible and $\rpt{j}{\phi}{\psi}$ is reducible at $i$ then if
$\rp{j'}{\phi'}_{\psi} \leftarrow \mathbf{reduce}(\sigma_i,\tau,i,\mathbb{S}^i_{\psi}, \rpt{j}{\phi}{\psi})$, $\rpt{j}{\phi'}{\psi}$ is correct/prompt/reducible.
\textit{Proof}. Proof by mutual induction. \\
%
$\mathbf{reduce}(\ldots)$ is trivially c/r/p for $\top,\bot$ residues. \\ \\
Case $\phi \equiv p$: Since the residue is reducible and there is a free proposition, we know that $i = j$. From definition of reduce, we'll get $\vDash \sigma_i(p) \leftrightarrow \vDash p$. \\ \\
Case $\phi \equiv \neg \psi_1$: Follows from correctness of reduce and simplify. \\ \\
Case $\phi \equiv \psi_1 \vee \psi_2$: Follows from correctness of reduce and simplify. \\ \\

## Slide 84: Reduce is correct (cont)
Notes: \textit{Proof}. Proof by mutual induction. \\
%
Case $\phi \equiv \alpha \mathcal{U}_{[l,h]} \beta$: Two subcases: $\vDash \phi \rightarrow \vDash \phi'$ and $\vDash \phi' \rightarrow \vDash \phi$ \\ \\
Subcase $\vDash \phi \rightarrow \vDash \phi'$: From semantics of $\mathcal{U}$ we know that there exists a $k$ where $\beta = \top$ in the bounds and for all $\tau_k'$ where $k' \in [j,k-1]$ we have $\alpha = \top$. Looking at the definition of reduce we see that $a_u \geq b_t$ so $\phi' = \top$. \\ \\
%
Subcase $\vDash \phi' \rightarrow \vDash \phi$: There are three sub cases here, $\phi' = \top, \bot, \phi$. The $\bot$ and $\phi$ cases are trivial so we look at the $\top$ case. In this case, $a_u \geq b_t$ and $b_t \neq 0$ so we know there exists a $k$ where $\tau_k \in [\tau_j+l,\tau_j+h]$ and $\rp{k}{\top} \in S^i_\beta$. Since $S^i_\beta$ is correct, we know that $\sigma, \tau, k \vDash \beta$. From $a_u$ we know that all $\forall k'.(\tau_j \leq \tau_k' < a_u).\rp{k'}{\tau} \in S^i_\alpha$. Since $S^i_\alpha$ is correct and $a_u \geq b_t$ we know that $\forall k'.(\tau_j \leq \tau_{k'} < b_t). \sigma, \tau, k' \vDash \alpha$. From the semantics of $\mathcal{U}$, we see that $\sigma, \tau, j \vDash \alpha \mathcal{U}_{[l,h]} \beta$.

## Slide 85: Reduce Promptness
Notes: \textbf{Proof.} Promptness of $\mathbf{reduce}(\ldots)$ requires that given $\rp{j}{\phi'}$ at step $i$, $(\tau_i - \tau_j) \geq \Delta^{\omega}(\psi) \rightarrow \phi' \in \{\top,\bot\}$. \\ \\
%
There are two top-level cases, either there is no true $\beta$ residue or a true $\beta$ residue exists. \\ \\
%
Subcase no-$\beta$: In this case, $\forall k. (\tau_{j}+l \leq \tau_k \leq \tau_j+h). \rp{k}{\bot} \in S^i_\beta$. If this is true and $\tau_i-\tau_j \geq \Delta^{\omega}(\psi)$ then we see from the definition of reduce that $b_n = \top$ and so $\phi' = \bot$. \\ \\
%
Subcase $\beta$ exists: In this case, $\exists k.(\tau_j+l \leq \tau_k \leq \tau_j+h). \rp{k}{\psi'} \in S^i_\beta$ and $\psi' \neq \bot$. Since $\tau_k \in [\tau_j+l,\tau_j+h]$ and $\tau_i-\tau_j \geq \Delta^\omega(\phi)$ we know that $\tau_i-\tau_k \geq \Delta^\omega(\beta)$ and so $S^i_\beta$ is prompt at $k$. This means that $\psi' = \top$. and then in $\mathbf{reduce}(\ldots)$, $b_a \leq k$ and $b_t = b_a$. \\ \\
%
From here we have to more sub cases, either $\alpha$ is true until $\beta$ or it's not. \\ \\
%
Subcase not $\alpha$ until $\beta$: In this case, if $\exists k' \in [j,b_a-1]. \rp{k}{\bot} \in S^i_{\alpha}$ then from the definition of $\mathbf{reduce}$ we can see that $a_a < b_a$ and so $\phi' = \bot$ \\ \\
%
Sub-Subcase $\alpha$ until $\beta$:
Otherwise, $\forall k' \in [j,b_a-1]. \rp{k}{\top} \in S^i_\alpha$ (due to promptness of $S^i_\alpha$). From the definition of $\mathbf{reduce}$ we can see that $a_u \geq b_a = b_t$ so $a_u \geq b_t$ and $\phi' = \top$.

## Slide 86: Discussion
Monitor correctness
  Implementation
  Input data
Consolidation
  Trade off isolation guarantees for cost

## Slide 87: Eval Lessons Learned
Optimizations matter for real-world performance
Specification quality depends heavily on documentation
Detection accuracy (esp. FP issues) depends on good specification
Specifications must also take initialization and modes into account
Notes: ----- Meeting Notes (1/13/15 22:54) -----
get rid of this slide too

## Slide 88: Monitor as Diagnostic Tool
Check that ACC attempts to recover headway
(VehInPath && HeadwayLT2s) -> <0,200> [0,100] ~ACCAccel
Found violations with this rule
  So loosened bound durations (500ms, then 1s eventually)
Most violations removed with this tuning, but a few still there
  Either our rule does not describe the desired behavior or there is a real problem here
  Need more design info to be sure, worth bringing up

## Slide 89: Embedded Monitor
$15 retail ARM based Dev board
Moderately overpowered for our needs
  Useful while we’re exploring
32-bit CPU up to 168Mhz
1MB flash, 192kb RAM, peripherals, etc